## Slide 1: FHWA Freight Intermodal Connectors Study
presented to
Advisory Committee on Supply Chain Competitiveness
April 16, 2015
presented by
Tiffany Julien, FHWA

## Slide 2: Agenda
Overview of Study
Key Findings from Literature Review
Discussion of Case Study Results
Approach for Analysis of Connector Conditions and Performance Task
Next Steps

## Slide 3: Overview of Study
Background
  List of National Highway System intermodal connectors developed in 1998
Purpose
  Develop information on use, condition, and performance of freight intermodal connectors
  Identify strategies and initiatives to improve connector condition and performance
Key Elements of Study
  Review literature and data on connectors
  Conduct 18 case studies
  Analyze use, condition, and performance of large sample of connectors
  Conduct local and national stakeholder outreach

## Slide 4: Literature Review Key Findings Growth by Freight Mode
Marine port and rail intermodal volumes have increased
Air cargo and barge volumes have remained relatively flat
Emergence of truck-truck terminals
  Supported by growth in warehousing employment
  Examples – Dallas Logistics Center in Texas; Pureland Ind. Complex in New Jersey; Coastal International Logistics in Florida
Year | U.S. Warehousing Employment | Percentage Change from 1998
1998 | 119,493 | –
2004 | 572,000 | 379%
2005 | 615,900 | 415%
2006 | 656,600 | 449%
2007 | 675,800 | 466%
2008 | 657,400 | 450%
2009 | 620,500 | 419%
2010 | 641,400 | 437%
2011 | 664,100 | 456%
2012 | 707,000 | 492%
2013 | 725,000 | 507%
2014 (Aug.) | 744,500 | 523%

## Slide 5: Literature Review Key Findings Data on Freight Intermodal Connectors
Number of freight intermodal connectors has increased for all modes since 2000
Economic and supply chain trends indicate that port, rail, and truck-truck intermodal facility volumes will continue to grow
Existing FHWA data sources can be used to estimate use, condition, and performance of most connectors
  Highway Performance Monitoring System (HPMS)
    Truck and auto volumes, pavement condition
  National Performance Management Research Data Set (NPMRDS)
    Vehicle probe data with truck and auto speeds on the designated National Highway System

## Slide 6: Case Studies Purpose
Document data availability for selected freight intermodal connectors
Estimate use, condition, and performance of select connectors
Identify planning efforts that incorporate the select connectors
  Focus on agency coordination
  Review process used for studies
  Determine how study results are incorporated into programming
Describe improvement projects and funding mechanisms targeted towards connector condition and performance

## Slide 7: Case Studies Number, Type, and Location
18 freight intermodal terminals
  60 freight intermodal connectors
Rail
Atlanta (GA) Inman Rail Yard
Edgerton (KS) Intermodal Railyard
Marion (OH) Intermodal Railyard
Chicago (IL) Area Consolidated Hub
Ports
Port of Baltimore (MD)
Port of Philadelphia (PA)
Port of Long Beach (CA)
Port of Savannah (GA)
Port of Catoosa (OK)
Port of Houston (TX)
Port of Cleveland (OH)
Port of Portland (OR)
Air Cargo
Memphis (TN) International Airport
Charlotte/Douglas (NC) International Airport
Portland (OR) International Airport
Emerging Industries
Williston (ND)
City of Industry (CA)
Port of Jacksonville (FL)

## Slide 8: Case Studies Process
Reviewed FHWA databases for all connectors
Reviewed state, MPO, and local sources
  Statewide – Long-Range Plans, Statewide Transportation Improvement Programs, and Freight Plans
  MPO, where applicable – Long-Range Transportation Plans, Congestion Management Processes, Transportation Improvement Plans, and Freight Plans
  Corridor studies, subarea studies, and freight facility studies
Interviewed local public- and private-sector stakeholders

## Slide 9: Case Study Findings Characteristics, Use, Condition, and Performance
Some local roads used as connectors are not officially designated
Roadway characteristics
  Most connectors are 2- to 4-lane local roads or arterials
  Short roadways – average length is 2.9 miles
Average Daily Connector Use – 12,500 vehicles and 1,600 trucks
Most connectors have worse pavement conditions than other similar roadways in their states
Over two-thirds of connectors experience congestion

## Slide 10: Case Study Findings Planning and Stakeholder Coordination
Planning
  Tools to estimate future intermodal conditions not widely used
  Studies that include connectors emphasized congestion and land use issues with pavement rarely mentioned
  No freight intermodal connector programs were identified
Stakeholder Coordination
  Connectors may be owned by states, counties, or cities and often span several local jurisdictions
  Motivation for freight intermodal connectors planning – states concerned about economic development, locals concerned about neighborhoods
  Stakeholder coordination relied heavily on freight champions

## Slide 11: Connector Conditions and Performance Analysis Approach
Connector Characteristics | Metric | Attributes to Test
Use | Total volumes Truck volumes | Type of terminal (port, railyard, barge, air cargo, or other) Functional classification Rural, urban, or suburban location Governmental ownership (state, local) Number of lanes, posted speeds, and number of railroad crossings
Condition | Pavement condition | 
Performance | Truck speeds by time of day | 
Determine use, condition, and performance of a sample of connectors

## Slide 12: Next Steps
Complete case study documentation
Analyze connectors condition and performance
Prepare recommendations and draft report
  Available summer 2015
Review draft report with national and local stakeholder groups and other national freight organizations

## Slide 13: Questions and Comments
For additional information, contact: Tiffany Julien FHWA Project Manager tiffany.julien@dot.gov